WDO Amendment #13

Pages 37-38 – WDO Article IV, Section C.2.d.

- Compensatory storage is required for all storage lost or displaced in a Regulatory Floodplain due to development.

Hydraulically equivalent compensatory storage requirements for fill or structures in a riverine Regulatory Floodplain shall be at least equal to 1.2 times the volume of Regulatory Floodplain storage lost or displaced.  Such compensation areas shall be designed to drain freely and openly to the channel and located opposite or adjacent to fill areas.  A deed or plat restriction is required to prohibit any modification to the compensation area.  The Regulatory Floodplain storage volume lost below the existing 10-year frequency flood elevation must be replaced below the proposed 10-year frequency flood elevation.  The Regulatory Floodplain storage volume lost above the 10-year existing frequency flood elevation must be replaced above the proposed 10-year frequency elevation.

Hydraulically equivalent compensatory storage requirements for fill or structures in a non-riverine Regulatory Floodplain shall be at least equal to 1.0 times the volume of Regulatory Floodplain storage lost or displaced.  Non-riverine floodplain storage may be replaced at or below the existing elevation but not below the Normal Water Level.

Upon approval of the Enforcement Officer, shorelines or streambanks that have experienced erosion may be restored to their condition as of the effective date of the first FIRM in that community without the need to provide compensatory storage or pay a fee-in-lieu of for the fill used to restore the eroded area according to the following criteria:

- The restoration fill shall meet existing grades and within riverine areas the current effective Regulatory Floodplain and Regulatory Floodway conveyance shall be maintained

The amount of eroded property being restored shall be documented and submitted by the applicant as part of the permit process.  Proper documentation shall be either field survey information or photo documentation of the erosion that has occurred for the property being restored.

For rivers, lakes and streams where no floodway has been designated, no documentation of past shoreline erosion is required if the applicant does not exceed 1 cubic yard of fill per lineal foot for a maximum of 200 feet.  In this case, the placing of the fill shall not significantly alter the alignment of the shoreline with adjoining properties as determined by the Enforcement Officer.  Non-documentable fills are a one-time allowance on a per property basis and all fills exceeding 200 cubic yards shall be regulated as specified in Articles IV.B.1.f. and IV.C.2.d. of this Ordinance.

Top dressing is the placement of not more than four (4) inches of topsoil within the Regulatory Floodplain.  fFor the purposes of stabilizing an existing erosion control problem or establishing vegetative cover., Ttop dressing shall be allowed by permit on a per-parcel, one-time only allowance, and not impact adjoining property drainage patterns.  Upon approval of the Enforcement Officer, floodplain compensatory storage shall not be required.  Top dressing fill shall comply with the Soil Erosion and Sediment Control standards and Wetlands Provisions of this Ordinance (Article IV.B.1.j. and IV.E.).  This provision shall not be applicable to the design process for new development.

Top dressing is the placement of not more than four (4) inches of topsoil within the Regulatory Floodplain.  For the purposes of restoring pre-subsidence grade to an area that primarily experiences subsidence due to a documented flood event, top dressing shall be allowed by permit on a per-parcel basis and not impact adjoining property drainage patterns.   Upon approval of the Enforcement Officer, floodplain compensatory storage shall not be required.  Top dressing fill shall comply with the Soil Erosion and Sediment Control standards and Wetlands Provisions of this Ordinance (Article IV.B.1.j. and IV.E.).  This provision shall not be applicable to the design process for new development.  Allowance of this provision shall be in accordance with the following criteria:

(a)	Repeat top dressing applications are limited to documented flood events with topographic or photographic evidence of subsidence.

(b)	The restoration fill shall meet pre-subsidence elevations, and within riverine areas, the pre-subsidence effective Regulatory Floodplain and Regulatory Floodway conveyance shall be maintained.

(c)	The damaged property being considered for top dressing shall be documented and submitted by the applicant as part of the permit process.  Proper documentation shall be either field survey information or photo documentation of the flooding and subsidence that has occurred on the property.

Upon completion of top dressing, the applicant shall provide topographic or photographic documentation of completed work.

Purpose:	To allow property owners to repair flood-damaged properties after flood events.  Long-standing flood waters cause subsidence and chemical breakdown of soil, creating depressed areas and preventing new vegetation growth.

TAC Vote:	8/21/08: Unanimously approved.

SMC Staff Modification to address public comment: 10/23/08