Title:

Applicability and Use Standards for Recycling Facilities Accepting Exclusively General Construction or Demolition Debris for Transfer, Storage, or Treatment.

Purpose & Intent:

The regulations within this article are intended to accomplish the following purposes:

- To establish location, design, operating and reporting criteria appropriate to assess the suitability and on-going compliance of a recycling facility proposed to accept exclusively general construction or demolition debris.

- To promote the safe and unobtrusive recycling of general construction or demolition debris from the waste stream.

Definitions:

“Applicant” is the person or corporate entity seeking to develop, permit, and operate a general construction or demolition debris recycling facility in accordance with this ordinance and the Act.

"Facility" is the tract of land including, but not limited to, buildings and improvements that are used solely for the purposes subject to regulation of this ordinance and the Act.

"General construction or demolition debris" means nonhazardous, uncontaminated materials resulting from the construction, remodeling, repair, and demolition of utilities, structures, and roads, limited to the following: bricks, concrete, and other masonry materials; soil; rock; wood, including nonhazardous painted, treated, and coated wood and wood products; wall coverings; plaster; drywall; plumbing fixtures; nonasbestos insulation; roofing shingles and other roof coverings; reclaimed or other asphalt pavement; glass; plastics that are not sealed in a manner that conceals waste; electrical wiring and components containing no hazardous substances; and corrugated cardboard, piping or metals incidental to any of those materials as defined in Section 3.160 (a) of the Act.

"Illinois Environmental Protection Act" as promulgated in 415 ILCS 5, herein referred to as the “Act”.

“Illinois Environmental Protection Agency” herein referred to as “IEPA”

“Illinois Natural Areas Inventory” herein referred to as “INAI”

Applicability:

This section applies to applicants of recycling facilities which will accept exclusively general construction or demolition debris, and are proposed to receive permit authority by the IEPA requiring compliance with Section 22.38 of the Act.  Such a facility shall be an approved special use within the (Industrial, Commercial, Manufacturing) Zoning Districts.  Applicants seeking to conduct recycling of exclusively general construction or demolition debris shall do so on parcels greater than (5) acres in size.

Use Standards:

Location Standards:

- The facility shall not be located within 300 feet of property zoned primarily for residential use (or dwelling) unless the residentially zoned property or dwelling is separated from the facility by a designated truck route, active rail line, high voltage power transmission easement or other clearly demarcated landuse planning transition boundary.

- The facility shall be located outside of the 100 year flood plain, or be flood-proofed.

- The facility shall not be located in jurisdictional wetlands.

- The facility shall not be located on a site of archeological, architectural or historical significance.

- The facility shall not be located in which threatened or endangered species are known to be present as identified by the INAI database.

Design Standards:

- Provide a Plat of Survey and legal description identifying the facility boundary for which general construction or demolition debris recycling activities are proposed to be permitted.

- Provide a site plan of the proposed facility which identifies, at a minimum, the following site features:

    - Access/egress point(s)

    - Parking areas

    - Any buildings, structures or fixed equipment

    - Extent of paved or impervious surfaces

    - Material tipping/receiving areas

    - Material processing areas

    - Areas of proposed material stockpiling (by material type)

    - Material loading areas

    - Fencing, berming or screening features

- Provide building elevations and/or descriptions of proposed buildings or structures as necessary to convey the architectural appearance and physical magnitude of the proposed improvements.

- The general construction or demolition debris receiving/tipping areas shall be constructed of a low permeability material (eg. Portland cement concrete, Asphalt concrete) such that it prevents infiltration and is able to withstand anticipated loads.

- The facility shall be equipped with a fence no less than eight (8) feet in height located to secure the operating areas of the facility during non-operating hours as well as assist in minimizing the potential for litter to leave the facility.

- The facility shall be equipped with a vehicle scale to weigh incoming deliveries and outbound shipments.

Operating standards:

The applicant shall provide an operating plan that demonstrates how the facility will comply with Section 22.38 of the Act.  The operating plan shall, at a minimum, contain the follow information:

- Number of employees anticipated at the facility.

- Proposed hours of operations for:

    - Receipt of general construction or demolition debris

    - Processing and shipment of general construction or demolition  debris

- Anticipated daily average / maximum volume (in tons) of general construction or demolition debris to be received at the facility.

- Identify as to if the facility will accept general construction or demolition debris deliveries from third-party haulers.  If so, describe the means by which third party haulers will be informed of what materials are acceptable at the facility.

- Identify the number of vehicles (by vehicle type) anticipated to utilize the facility on a daily basis and demonstrate that the facility as proposed minimizes the impact on area roadways.

- Describe the method and equipment utilized to separate the recyclable general construction or demolition debris from the non-recyclable general construction and demolition debris within 48 hours of its receipt.

- Describe the procedures by which all non-recyclable general construction or demolition debris will be removed and disposed of within 72 hours of its receipt.

- Describe any processing equipment (ie grinders/shredders/balers) proposed to be utilized to prepare the recyclable general construction or demolition debris for stockpiling or shipment.   Describe the design or operating controls proposed to be implemented so as to comply with applicable noise standards.

- Describe operating methods employed to control odor, combustion of materials, vectors, dust, and litter.

- Describe the method and equipment utilized to load recyclable and non-recyclable general construction or demolition for shipment from the facility.

- Identify which activities are proposed to be conducted indoors or under cover.

- Provide typical and maximum anticipated height of stockpiled recyclable construction or demolition debris for each recyclable material by type.  Discuss the buffering and/or screening measures employed to minimize the visual impact of the proposed stockpiles from surrounding land uses.

- Identify any other proposed site uses (such as truck storage/maintenance/fueling/container storage) and demonstrate that they can be conducted in a safe and unobtrusive manner without interfering with safe general construction or demolition debris recycling activities.

Operator Experience:

The applicant shall provide information / description of the following:

- Experience in operating material recovery facilities which require the marketing and shipment of numerous recyclable commodities.

- Describe the proposed end-use markets for separated general construction or demolition debris to demonstrate compliance with the diversion requirements of Section 22.38 of the Act.

Regulatory/Reporting Standards:

The applicant shall provide information / description of the following:

- Identify all regulatory permits necessary to operate the facility as proposed.

- Discuss the material tracking methods and recordkeeping to be employed to demonstrate compliance with Section 22.38 of the Act.  Records shall be tabulated (monthly) and made available to the (Village/City/County) on a (quarterly) basis to demonstrate compliance with Special Use.

- All records shall be maintained for a period of at least (3,5,7) years.  The period shall be longer in the event of a dispute.

- Provide a closure plan and closure cost estimate for the facility.